## Slide 1: Tcl/Tk Tools for EPICS Control Systems
Ron Fox
National Superconducting Cyclotron Laboratory
Notes: Note this effort was a WIP last year. Now it represents stable released work in use at the NSCL.

## Slide 2: Outline
What is EPICS?
Prior work interfacing Tcl/Tk to EPICS
Why a new interface?
What the new interface looks like?
A gallery of EPICS aware widgets.

## Slide 3: EPICS
Experimental physics and industrial control system (www.aps.anl.gov/epics)
Distributed control system
  IOC attached or talks to hardware
  Client nodes provide user interface
Intended use:
  Accelerator controls
  Experiment slow controls
Notes: Built by a consortium of accelerator labs.. Primarily ANL and LANL.
NSCL uses this for
Accelerator controls
Beamline controls
Some experimental apparatus controls.
PLCs are integrated into the system… as well as individual non PLC devices (e.g. beam current monitors, magnet power supply controllers etc.).

## Slide 4: A Typical EPICS installation
IOC
IOC
IOC
IOC
…
…
gateway
Console systems
Notes: IOC’s attach to or contact hardware.
Console systems are used by users of the control system (control panels etc.).
Usually Epics runs on its own routed subnet, or a private subnet and the gateway
Allows controlled access to the control system outside that subnet.
Epics has a highly developed acl/ace based permission system that extends to individual channels.

## Slide 5: A Typical EPICS installation
IOC
NA
Device
…
PLC
Notes: Increasingly devices are network attached and IOC’s are really
Epics/device protocol translators and gateways to other nested private subnets for the devices themselves.
(NSCL Home built controllers are now based on Z-world processor systems all with on-board Ethernet.
Programmable Logic Controllers are also in widespread use in the epics community.

## Slide 6: Prior Art
Et - http://www.aps.anl.gov/epics/EpicsDocumentation/ExtensionsManuals/TclTk/et.tcltk.html
  Extended wish shell with epics knowledge
  Requires blt
  Use is not so Tcl-ish.
it-wish – http://www.aps.anl.gov/epics/EpicsDocumentation/ExtensionsManuals/TclTk/it.tcltk.html
  Extends etwish – with access to idl.
  Not a package
  Same epics interface as et.

## Slide 7: Why Tcl and Epics
Experimenters need to access EPICS information:
  Some experimental device controls are EPICS based.
  For some experiments, knowing beam line settings is important in analyzing data.
Side issues:
  Technology evangelism in the NSCL controls group because:
  Controls group wants to move away from win only UI’s.
  Operators are not happy with the UI’s they have and with how long it takes to modify old UI’s an to build new ones.

## Slide 8: What we wanted:
Loadable Tcl (Tk) package.
  Distribute control apps as starkits/starpacks (stubs enabling).
Transparent mapping of tcl variables to epics process variables.
Better support for ‘strange’ EPICS channel types:
  Enumerated types.
  Array types.
Tcl-ish style interfaces.
Control widget set.
  Base generic control widgets.
  Epics aware widgets.
Notes: And other things like cross platform portability of the user interface
NCSApps + Controls group disillusionment with Windows.
Put console specification and generation in the hands of those who have to use them.
Side note about NSCL controls group, Qt, Tcl, Operators actively building
Applications.

## Slide 9: Architecture
CA
Tcl/Tk & stubs lib.
EpicsTcl
controlwidget
epicswidgets
Application
Interpreter
Notes: Controlwidget and epicswidgets are snidgets.
Ideally you want:
The application to live entirely on top of epicswidgets.
Failing that entirely on epicswidgets epicstcl and maybe some controlwidgets but still pure tcl.
Failing that user written compiled extensions that can touch Tcl/Tk and/or CA – epics channel access library.

## Slide 10: Epicstcl features
Can connect to any EPICS process variable
Supports EIAS programming for EPICS channels.
Channel pooling.
Multi-way variable links
Thread-safe
Notes: Channel and multiway linking
Programming in the large/team programing necessities ..
If one part of the application connects to an epics channel, and another part subsequently connects to the same channel, the old link is used.. Reference counting determines when the actual link is broken
More than one variable can be linked to a channel. When a channel is updated all linked vars are updated. If any variable is written traces fire forcing a set to the linked channel. Multiple links of the same variable use reference counting to prevent premature unlinking.
Threadsafeness is a requirement of epics/tcl as epics notifications for PV updates occur in an arbitrary thread and the extension has to therefore turn these into cross thread events to synchronize with the interpreter’s event loop.

## Slide 11: Epicstcl for scripters:
Object model construct a channel:
epicschannel pvname

## Slide 12: Epicstcl for scripters:
pvname get ?count?
pvname set value-list ?format?
pvname link tclVariableName
pvname unlink tclVariableName
pvname listlinks ?pattern?
pvname updatetime
pvname values
pvname size
pvname delete
Notes: Set …?count? – returns at most the first count entries of an array channel.
Unlink - really decs a reference count, doing the unlink when the refcount goes to zero.
Updatetime – when did epics last post an update event to us for this channel.
Delete – Also decerements a reference count.
Values - describes the legal values. For ‘normal’ data may be string, int, float or a list of legal enum strings for
enumerated channel types.
Size – Number of elements in the array (1 if the channel is a scalar).

## Slide 13: Control Widgets
meter
led
typeNGo
radioMatrix
Notes: Controlwidgets are just snidgets.
They look very much like any other Tk widget… using -variable –command
Switches to connect to application logic. They are not dependent on the use of
EPICS.

## Slide 14: Epics Aware widgets
snidgets (in many cases extending the functionality of the control widgets on the previous slide)…. Or snit::widgetadaptor
-channel switch for most links the widget to an epics process variable (channel).
Widgets transparently DWII (do what I intend).
Notes: For many control applications, you want to do just
Link a set of graphical widgets to channels…

## Slide 15: Epics Aware Widgets
epicsLabel
epicsLabelWithUnits
CODE:
epicsLabel .l -channel Z001F-C
epicsLabelWithUnits .lu –channel Z001F-C
pack .l .lu
Notes: In all examples I’m leaving out the package require and namespace imports for brevity.

## Slide 16: Epics aware widgets
Code:
epicsMeter .m –channel Z001F-C
epicsBCMMeter .bm \
-channel Z001F-C
pack .m .bm –side right
Notes: Left is just the meter widget -> epicsmeter, right is a BCMMeter.. Futher specialized to view channels that have range adjustments
(up/down arrow buttons).

## Slide 17: Epics aware widgets
epicsButton
(single)
epicsButton
(double)
epicsCommandButton
Code:
epicsButton .b1 –channel IGBI0
epicsButton .b2 –channel IGBI0 \
-modality double
epicsCommandButton .b3 –channel IGBI0 \
-value 1 –text on \
-background red
Notes: Labels for the epicsButtton can be supressed as well…

## Slide 18: Epics Aware Widgets
epicsLed
epicsEnumeratedControl
Code
epicsLed .led –channel IGBI1 –on red –off green \
-showlabel true
epicsEnumeratedControl .ec –channel IGBI1 \
-values {{on 1} {off 0}}
pack .led .ec –side left
Notes: Enumerated control example is a bit simplistic, but in many of our devices, there are ‘multistate’ objects… e.g. a target ladder with specific positions corresponding to setting a specific target into the accelerator beam.. Or in the coupling line stripper foil, specific positions of a chain drive placing specific stripper foils into the injection line beam and more and more…
Enumerated control values list… each element can be a single element.. In which case it doubles as the
Label and value. Or a 2 element list in which case first is the label the second the value of the channel
Epics aware pulldown menus and spin boxes also exist to support enumerated types.

## Slide 19: Epics Aware Widgets
CODE:
epicsStripChart .e
.e yaxis configure –min 0.0 –title Temperature
.e xaxis configure –autorange 500 –shiftby 10.0 \
-title Time
.e grid on
.e legend configure –position bottom
.e addchannel TI9400 500 –symbol {}
pack .e
Notes: NSCL has a temp sensor outside of it’s cyroplant.. Sorry .. It gives the temp. in Fahrenheit.
If you wanted to monitor the time evolution of this temperature you could write code like the
Above.
epicsStripChart extends BLT’s stripchart widget.. So most of the above is delegations to
BLT’s stripchart.
.e addchannel … adds a trace to the strip chart of an epics channel sampled every n ms.
Remaining configuration options are passed uninterpreted to BLT’s data series configuration.
Any number of data series can be added to the strip chart…and in fact Epics/non epics
Series can be intermingled if you know the BLT stripchart widget.

## Slide 20: Epics Aware Widgets
Notes: Here’s the temp profile from early morning 8/28/2007:
Note that as you’d expect as the sun comes up, the temperature slowly edges upwards.

## Slide 21: Status of work
Ported to all NSCL epics platforms:
  Linux-x86
  Mac OS-X
  Windows XP/2000
NSCL Control system group is uninterested.
  “Tcl/Tk is not in our skill set.”
  “We will build our portable apps using Qt.”
Operators are enthusiastically using it.
NSCL Assoc. Director of Operations:
  “Operators will build the next generation of console apps.”